# Eclipse i Arduino
https://www.youtube.com/watch?v=TtPvkPpAx0E
https://links2004.github.io/Arduino/d4/dec/md_esp8266_doc_eclipse_eclipse.html
https://www.youtube.com/watch?v=AMyyAFkSj60
0. Instalirati Arduino
1. Instalirati Eclipse IDE for C/C++ Developers
2. Help -> Eclipse Marketplace
3. U tražilicu upisati "Arduino"
4. Instalirati "The Arduino Eclipse plugin named Sloeber V4"
5. U Arduino folderu napraviti sljedeće:
cd hardware
mkdir esp8266com
cd esp8266com
git clone https://github.com/esp8266/Arduino.git esp8266
cd esp8266/tools
python get.py
6. Otvoriti "Arduino perspektivu"
7. Project Explorer -> desni klik -> New -> Arduino Sketch:

9. $ sudo apt install esptool
# Instalacija ESP8266
U "Datoteka > Preporučene vrijednosti" dodati http://arduino.esp8266.com/stable/package_esp8266com_index.json:

Alati -> Pločica -> Boards Manager -> esp8266

# Terminal
~$ sudo chown bmlikota /dev/ttyUSB0
## ESP8266
- to je bežični SoC (system on a chip) - mikroćip koji ima sve komponente kompjutera
- ima GPIO, I2C, ADC, SPI, PWM...
- CPU default je 80MHz, maksimalno može biti 160MHz
- baziran je na RISC arhitekturi
- jezgra je 106micro Diamond Standard core (LX3) - made by Tensilica
# UART (universal asynchronous receiver-transmitter)
- računalni hardverski uređaj za asinkrono serijsko komuniciranje
- format podataka i brzina prijenosa je konfigurabilna
- standardno se stavljaju u mokrokontrolere
- uzima bajtove i transmitira ih u bitovima jedan za drugim (to je serijska transmisija kroz jednu žicu), a na odredištu drugi UART prima bitove i slaže ponovo u bajtove
# SoftAP
- je skraćenica od "software enabled access point" je virtualni ruter – omogućuje da računalo, koje nije specificirano za to, postane wireless pristupna točka
- SoftAP pretvara ESP8266 u pristupnu točku preko koje se povezujete na WiFi
- Station mod pretvara ESP8266 u stanicu, tj. povezat će se na WiFi mrežu specificiranu u kodu
"Once you start working with ESP module, you would come across these two terms frequently. Let us say you and your friend would like to surf the internet on your smart phones but since he does not have an active internet connection you decide to turn on your hotspot and your friend connects to it. Here your phone which is sourcing the internet connection is the Access Point (AP) and your friend’s phone which is using the internet is called the Station (STA)."

# DHCP (Dynamic Host Configuration Protocol)
Mrežni je protokol korišten od strane mrežnih računala za dodjeljivanje IP adresa i ostalih mrežnih postavki kao što su pretpostavljeni gateway, subnet maska i IP adrese DNS servera s DHCP servera. Olakšava konfiguraciju mreže jer eliminira ručno dodavanje osnovnih postavki za jednu računalnu mrežu. DHCP klijent se brine da su dodijeljene IP adrese ispravne i da u mreži nema sukoba adresa.
# TCP
TCP je jedan od osnovnih protokola unutar IP grupe protokola. Naziv je kratica od engleskog naziva Transmission Control Protocol. Korištenjem protokola TCP aplikacija na nekom od hostova umreženog u računalnu mrežu kreira virtualnu konekciju prema drugom hostu, te putem te ostvarene konekcije zatim prenosi podatke. Stoga ovaj protokol spada u grupu tzv. spojnih protokola, za razliku od bespojnih protokola kakav je primjerice UDP. TCP garantira pouzdanu i isporuku podataka u kontroliranom redoslijedu od pošiljatelja prema primatelju. Osim toga, TCP pruža i mogućnost višestrukih istovremenih povezivanja prema jednoj aplikaciji više klijenata na jednom hostu više klijenata, gdje su najčešći primjeri za to web ili poslužitelji e-pošte.
# UDP
UDP (User Datagram Protocol) je protokol koji se nalazi u dijelu transportne razine OSI modela, te je uz TCP jedan od temeljnih Internet protokola. UDP omogućuje slanje kratkih poruka (datagram) između aplikacija na umreženim računalima. U odnosu na mrežnu razinu OSI modela UDP dodaje samo funkcije multipleksiranja i provjeravanja pogreške prilikom prenošenja podataka, a nema mogućnost provjere primitka poruke jer ne čuva informaciju o stanju veze (tj. radi na principu pošalji i zaboravi). Zbog toga se koristi kada je bitnija brzina i efikasnost od pouzdanosti, npr. za prijenos govora u realnom vremenu (VoIP telefonija), a također i kada je potrebno slanje iste poruke na više odredišta (multicast).
# SparkFun Logic Level Converter - Bi-Directional

- The SparkFun bi-directional logic level converter je mali uređaj koji sigurno prevodi signal od 5V u signal od 3.3V i obratno signal od 3.3V prevoid u signal od 5V.
# Povezivanje komponenti
# TX i RX
- TX je transmit signala. To je snaga u "decibel po milivatima" (-13 dBm po defaultu) po kojoj modem transmitira signal.
- RX je za primanje signala (recieve). To je snaga u dBm (od -18 do -25) od dolaznog signala.
## AT instrukcije
- komande za modeme, nebitno dali su u pitanju modemi koji se nalaze u mobilnim telefonima ili kao interni/eksterni u računalim
- kod mobilnih telefona starijih generacija modem ima serijski izlaz, pa je zgodan za korištenje sa mikrokontrolerima. kod novijih telefona kada se telefon ukljuci u usb postoji negdje opcija da se kreira virtuelni serijski port koji sluzi za pristup modemu u telefonu
- ESP8266 se povezuje na drugi MCU (multipoint control unit)
- preko UART-aMCU šalje AT+CMD preko UART-a da bi kontrolirao ESP8266

Svaka instrukcija može sadržavati četiri komande:
1. Test – AT+CMD=? - provjerava da li je komanda postavljena ili parametre i njihov range
2. Query – At+CMD? - vraća trenutnu vrijednost parametra
3. Set – AT+CMD=Parameter – postavlja vrijednost koju je korisnik definirao i pokreće komandu
4. Execute – AT+CMD – pokreće komandu bez parametara koje je definirao korisnik
Napomene:
- nemaju sve AT instrukcije četiri komande
- [] = defaultna vrijednost
- string vrijendosti zahtjevaju duple navodnike, npr.: AT+CWSAP=“ESP756190”,”21030826”,1,4
- Baud rate = 115200 (jedinica brzine transmisije = broj koliko puta signal promijeni stanje u sekundi; 1 baud je ekvivalentan jednom bitu po sekundi)
- AT instrukcija završava s “\r\n”
## Osnovne AT instrukcije
- AT – testira da li je AT startan
- AT+RST resetira modul
- AT+GMR – informacije o modulu
- AT+GSLP – ulazak u deep sleep mod
- ATE – echo AT komandi
### AT
Type	Instruction	Response
execute	AT	OK

### AT+RST – Restart module
Type	Instruction	Response
execute	AT+RST	OK

### AT+GMR – View version info
Type	Instruction	Response	Parameter
execute	AT+GMR	number OK	number:version info, length:8 bytes

### AT+GSLP – Enter deep-sleep mode
Type	Instruction	Response	Parameter
set	AT+GSLP=time	time OK	time : ms , set the sleep time of ESP8266 in ms.

### ATE – AT commands echo
Type	Instruction	Response
set	ATE	OK

Opis
ATE0 : Disable echo
ATE1 : Enable echo

## WIFI Function
Instruction	Description
AT+CWMODE	WIFI mode（station/softAP/station+softAP）
AT+CWJAP	Connect to AP
AT+CWLAP	Lists available APs
AT+CWQAP	Disconnect from AP
AT+ CWSAP	Set parameters under AP mode
AT+ CWLIF	Get station’s ip which is connected to ESP8266 softAP

### AT+CWMODE - WIFI mode（station/softAP/station+softAP）
Type	Instruction	Response	Function
Query	AT+CWMODE?	+CWMODE:mode OK	Query AP’s info which is connect by ESP8266.
Execute	AT+CWMODE=mode	OK	Set AP’s info which will be connect by ESP8266.

Opis parametara
- mod：
1 Station mod
2 SoftAP mod
3 SoftAP + Station mod

### AT+CWJAP – Connect to AP

Type	Instruction	Response	Function
Query	AT+CWJAP?	+ CWJAP:ssid OK	Query AP’s info which is connect by ESP8266.
execute	AT+CWJAP=ssid,pwd	OK	Set AP’s info which will be connect by ESP8266.

Opis parametara：
ssid： string, AP’s SSID
pwd： string, MAX: 64 bytes
Primjer：
AT+CWJAP="wifi-1","12345678"
### AT+CWLAP - Lists available APs
Type	Instruction	Response	Function
Set	AT+CWLAP=ssid,mac,ch	+CWLAP:ecn,ssid,rssi,mac OK	Search available APs with specific conditions.
execute	AT+CWLAP	+CWLAP:ecn,ssid,rssi,mac OK	Lists all available APs.

Opis parametara：
ecn:
0 OPEN
1 WEP
2 WPA_PSK
3 WPA2_PSK
4 WPA_WPA2_PSK
ssid: string, SSID od AP
rssi: jačina signala
mac: string, MAC adresa
### AT+CWQAP - Disconnect from AP
Type	Instruction	Response	Function
execute	AT+CWQAP	OK	Disconnect from AP

### AT+ CWSAP – Configuration of softAP mode
Type	Instruction	Response	Function
Query	AT+CWSAP?	+CWSAP:ssid,pwd,chl,ecn OK	Query configuration of ESP8266 softAP mode.
Set	AT+CWSAP=ssid,pwd,chl,ecn	OK	Set configuration of softAP mode.

Opis parametara
ssid: string, ESP8266 softAP’ SSID
pwd: string, MAX: 64 bytes
chl: channel id
ecn:
0 OPEN
2 WPA_PSK
3 WPA2_PSK
4 WPA_WPA2_PSK
Primjer
AT+CWSAP="esp_123","1234567890",5,3
### AT+ CWLIF– ip of stations which are connected to ESP8266 softAP
Type	Instruction	Response	Function
execute	AT+CWLIF	ip addr OK	Get ip of stations which are connected to ESP8266 softAP

Parameter description：
ip addr: ip address of stations which are connected to ESP8266 softAP
### AT+CWDHCP - Enable/Disable DHCP
Type	Instruction	Response
Set	AT+CWDHCP=mode,en	OK

Parameter Description
mode
0 : set ESP8266 softAP
1 : set ESP8266 station
2 : set both softAP and station
en
0 : Disable DHCP
1 : Enable DHCP
### AT+CIPSTAMAC - Set mac address of ESP8266 station
Type	Instruction	Response	Function
Query	AT+CIPSTAMAC?	+CIPSTAMAC:mac OK	Query mac info of ESP8266 station.
Execute	AT+CIPSTAMAC=mac	OK	Set mac of ESP8266 station.

Parameter Description
mac： string,mac info of ESP8266 station.
Example
AT+CIPSTAMAC="18:aa:35:97:d4:7b"
### AT+CIPAPMAC - Set mac address of ESP8266 softAP
Type	Instruction	Response	Function
Query	AT+CIPAPMAC?	+CIPAPMAC:mac OK	Get mac address of ESP8266 softAP.
Execute	AT+CIPAPMAC=mac	OK	Set mac of ESP8266 softAP.

Parameter Description
mac： string, mac address of ESP8266 softAP.
Example
AT+CIPAPMAC="2c:aa:35:97:d4:7b"
### AT+CIPSTA - Set ip address of ESP8266 station
Type	Instruction	Response	Function
Query	AT+CIPSTA?	+CIPSTA:ip OK	Get ip address of ESP8266 station.
Execute	AT+CIPSTA=ip	OK	Set ip addr of ESP8266 station.

Parameter Description
ip： string, ip address of ESP8266 station.
Example
AT+CIPSTA="192.168.101.108"
### AT+CIPAP - Set ip address of ESP8266 softAP
Type	Instruction	Response	Function
Query	AT+CIPAP?	+CIPAP:ip OK	Get ip address of ESP8266 softAP.
Execute	AT+CIPAP=ip	OK	Set ip addr of ESP8266 softAP.

Parameter Description
ip： string, ip address of ESP8266 softAP.
Example
AT+CIPAP="192.168.5.1"
## TCPIP Function
### AT+ CIPSTATUS – Information about connection
Type	Instruction	Response	Function
execute	AT+CIPSTATUS	STATUS:stat +CIPSTATUS:id,type,addr,port,tetype OK	Get information about connection.

Parameter description：
- stat：
- 2: Got IP
- 3: Connected
- 4: Disconnected
- id： id of the connection (0~4), for multi-connect
- type： string, “TCP” or “UDP”
- addr： string, IP address.
- port： port number
- tetype：
  - 0: ESP8266 runs as client
  - 1: ESP8266 runs as server
### AT+CIPSTART – Establish TCP connection or register UDP port and start a connection
Type	Instruction	Response	Function
Set	AT+CIPSTART=type,addr,port	OK	Start a connection as client. (Single connection mode)
Set	AT+CIPSTART=id,type,addr,port	OK	Start a connection as client. (Multiple connection mode)

Param description:
- id: 0-4, id of connection
- type: string, “TCP” or “UDP”
- addr: string, remote ip
- port: integer, remote port
### AT+CIPSEND – Send data
Type	Instruction	Response	Function
Set	AT+CIPSEND=length	SEND OK	Set length of the data that will be sent. For normal send (single connection).
Set	AT+CIPSEND=id,length	SEND OK	Set length of the data that will be sent. For normal send (multiple connection).
Execute	AT+CIPSEND

### Normal Mode
Parameter description：
id: ID no. of transmit connection
length: data length, MAX 2048 bytes
### Unvarnished Transmission Mode
Wrap return “>” after execute command. Enters unvarnished transmission, 20ms interval between each packet, maximum 2048 bytes per packet. When single packet containing “+++” is received, it returns to command mode.
### AT+CIPCLOSE – Close TCP or UDP connection
Type	Instruction	Response	Function
Set	AT+CIPCLOSE=id	OK	Close TCP or UDP connection.For multiply connection mode
execute	AT+CIPCLOSE	OK	Close TCP or UDP connection.For single connection mode

Parameter description：
id： ID no. of connection to close, when id=5, all connections will be closed.
(In server mode, id=5 has no effect)
### AT+CIFSR – Get local IP address
Type	Instruction	Response	Function
Execute	AT+CIFSR	+CIFSR:IP_address +CIFSR:IP_address OK	Get local IP address.

Parameter description：
IP_address:
IP address of ESP8266 softAP
IP address of ESP8266 station
### AT+CIPMUX – Enable multiple connections or not
Type	Instruction	Response	Function
Set	AT+CIPMUX=mode	OK	Set connection mode, single connection or multiple connection.

Parameter description：
mode:
- 0: single connection
- 1: multiple connection
NOTE
This mode can only be changed after all connections are disconnected. If server is started, reboot is required.
### AT+CIPSERVER – Configure as server
Type	Instruction	Response	Function
Set	AT+CIPSERVER=mode[,port]	OK	Configure ESP8266 as server

Parameter description：
- mode:
- 0: Delete server (need to follow by restart)
- 1: Create server
- port: port number, default is 333
NOTE
1. Server can only be created when AT+CIPMUX=1
2. Server monitor will automatically be created when Server is created.
3. When a client is connected to the server, it will take up one connection，and be provided an ID
### AT+CIPMODE – Set transfer mode
Type	Instruction	Response	Function
Set	AT+CIPMODE=mode	OK	Set transfer mode,normal or transparent transmission.

Parameter description：
- mode:
- 0: normal mode
- 1: unvarnished transmission mode
### AT+CIPSTO – Set server timeout
Type	Instruction	Response	Function
Query	AT+CIPSTO?	+CIPSTO:time	Query server timeout.
Set	AT+CIPSTO=time	OK	Set server timeout.

Parameter description：
time: server timeout, range 0~7200 seconds
### AT+CIUPDATE – update through network
Type	Instruction	Response	Function
execute	AT+CIUPDATE	+CIPUPDATE:n OK	Start update through network

Parameter description：
-n:
- 1: found server
- 2: connect server
- 3: got edition
- 4: start update
### +IPD – Receive network data
Type	Instruction	Response	Function
execute		+IPD,len:data	Receive network data from single connection.
execute		+IPD,id,len:data	Receive network data from multiple connection.

Parameter description：
- id: id no. of connection
- len: data length
- data: data received
### IPR
execute	response	Information
AT+IPR=Baud	OK/ERROR	Sets baudrate of ESP module

Don't use this command on newer firmwares! Configuration will be wrong and you will have to erase the configuration part of flash memory.
See UART_CUR and UART_DEF commands.
# at_example_0020000903
## Single connection
### (ESP8266 as TCP client)
1. Set wifi mode：
   AT+CWMODE=3 // softAP+station mode
   Response：OK
2. Reboot to take effect:
   AT+RST
   Response：OK
3. Connect to router
   AT+CWJAP="ssid","password" // ssid and password of router
   Response：OK
4. Query device’s IP
   AT+CIFSR
   Response：192.168.3.106 // Device got an IP from router.
5. Using a network tool (eg: ”NetAssist.exe”) on the computer to create a server.
   For example, server ip address:192.168.3.116, port 8080
6. ESP8266EX connect to server as a client
   AT+CIPSTART="TCP","192.168.3.116",8080 //protocol、server IP & port
   Response：OK
7. Send data
   AT+CIPSEND=4 // set date length which will be sent, such as 4 bytes
   >DGFY // enter the data, no CR
   Response：SEND OK
   Note: If the number of bytes sent is bigger than the size defined (n), will reply busy, and after sending n number of bytes, reply SEND OK.
8. Receive data:
   +IPD,n:xxxxxxxxxx // received n bytes, data=xxxxxxxxxxx
### Transparent transmission
1. Set wifi mode：
   AT+CWMODE=3 // softAP+station mode
   Response：OK
2. Connect to router
   AT+CWJAP="ssid","password" // ssid and password of router
   Response：OK
3. Query device’s IP
   AT+CIFSR
   Response：192.168.101.105 // Device’s ip that got from router.
4. Using a network tool (eg: ”NetAssist.exe”) on the computer to create a server.
   For example, server ip address:192.168.101.110, port 8080
5. Device connect to server
   AT+CIPSTART="TCP","192.168.101.110",8080 // protocol、server IP & port
   Response：OK
   Linked
6. Enable transparent transmission mode
   AT+CIPMODE=1
   Response：OK
7. Start send
   AT+CIPSEND
   Response： >
   Note: From now on, data received from uart will be transparent transmited to server.
8. Stop send
   Data packet contains only “+++” exits Unvarnished transmission.
## Multiple connection
### (ESP8266 as TCP server)
1. Set wifi mode：
   AT+CWMODE=3 // softAP+station mode
   Response：OK
2. Enable multiple connection
   AT+CIPMUX=1
   Response：OK
3. Setup server
   AT+CIPSERVER=1 // default port = 333
   Response：OK
4. PC connects to ESP8266EX softAP as station, then PC connects to ESP8266EX server as client.
   NOTE: ESP8266EX acting as server has a timeout mechanism. When connection is established and no data is transmitted within a period of time, it will disconnect the client. Please setup a recurring packet transmission every 5s on the computer to ensure connection is maintained.
5. Send data
   AT+CIPSEND=4 // set date length which will be sent, such as 4 bytes
   >iopd // enter the data, no CR
   Response：SEND OK
   Note: If the number of bytes sent is bigger than the size defined (n), will reply busy, and after sending n number of bytes, reply SEND OK.
6. Receive data: +IPD,n:xxxxxxxxxx // received n bytes, data = xxxxxxxxxx
### UDP transmission
1. Set wifi mode：
   AT+CWMODE=3 // softAP+station mode
   Response：OK
2. Connect to router
   AT+CWJAP="ssid","password" // ssid and password of router
   Response：OK
3. Query device’s IP
   AT+CIFSR
   Response：+CIFSR:STAIP,"192.168.101.104" // IP address of ESP8266 station
4. PC connects to the same router which ESP8266 connects to. Using a network tool (eg: ”NetAssist.exe”) on the computer to create UDP .
5. Enable multiple connection
   AT+CIPMUX=1
   Response：OK
6. Create a UDP transmission, for example, id is 4.
   AT+CIPSTART=4,"UDP","192.168.101.110",8080,1112,0
   Response：4,CONNECT OK
   Note：
   "192.168.101.110",8080 here is the remote ip and port of UDP transmission which create on PC in step 4;
   1112 is the local port of ESP8266, user-define, if user does not define it, it will be a random value;
   0 means destination peer entity of UDP will not change. For example, in this case, if another PC also creates a UDP entity and sends data to ESP8266 port 1112, ESP8266 can receive these data, but when we send data with command “AT+CIPSEND=4,X”, it will still be sent to the first PC. If this parameter is not 0, it will send to the new PC.
7. Send data
   AT+CIPSEND=4,5 // Send 5 bytes to transmission NO.4
   Response > DGFYQ // enter the data, no CR
   SEND OK
   Note: If the number of bytes sent is bigger than the size defined (n), will reply busy, and after sending n number of bytes, reply SEND OK.
8. Receive data:
   +IPD,4,n:xxxxxxxxxx // received n bytes, data=xxxxxxxxxxx
9. Delete transmission NO.4
   AT+CIPCLOSE=4
   Response：4,CLOSED OK